Content

# General
The device waits for a USB MIDI data packet to be received on one port and once this happens, the packet is send out on the other port. Until that transfer has finished, receiving of further packets is blocked temporarily. There is no internal buffering, rather the transfers are in real-time, one at a time.
This all happens for both directions independently and simultaneously.
## Packet Latency
The typical transfer time for the typical short MIDI packet is about 100µs in either direction, assuming very little other loads on the two USB busses.
When a packet could be sent within less than 1.2ms, the transfer is considered REALTIME.
When a packet could be sent within 1.2ms and 10ms, the transfer is considered LATE.
When a packet could be sent only after more 10ms, the transfer is considered STALE.
## Dropped Packets
When a packet cannot be sent in due time, the transfer is considered DROPPED and will be aborted. This may happen either when the outgoing port is not connected/ready or the host computer is currently not reading data within due time, stalling the transfer.
When the outgoing port is not ready the packet is dropped immediately.
When the port is ready a first stalling condition occurs, a timeout of 1s is used and the packet is dropped, for subsequent stalling packets, the timeout is reduced to 100ms. It then takes one successful packet delivery to reset the timeout to 1s again.
# Indicators
Each port side has a RGB (true color) LED indicator which shows both the port status and the packet status while a packet is running through. Each port LED is referring to the incoming data on that port.

The LED color basically shows the latency range measured for current and/or recent packet delivery.
The LED is flashing when an actual packet is running through the device.

## Continuous Port Status Display (dim colors)
The dim color of the LED represents the current status of the port :
Pulsing blue (slowly blinking, 3s period)	: port is not connected
Pulsing cyan (slowly blinking, 3s period)	: port is connected and receives USB power, but no USB communication is present.
Green	: port is connected and USB communication is ready to go.
Yellow	: port is connected and USB communication is ready to go, but there were LATE packets within the last two seconds.
Red	: port is connected and USB communication is ready to go, but there were STALE packets within the last four seconds.
Magenta	: port is connected and USB communication is ready to go, but there were DROPPED packets (with data loss) within the last six seconds.

## Flashing Packet Status Display (bright colors)
Green	: packet is running for less than 1.2ms (REALTIME).
Yellow	: packet is running for less than 10ms (LATE).
Red	: packet is running for more than 10ms (STALE).
Magenta	: packet had to be dropped.

NOTE: Because the actual transfer times are normally very short (< 100µs) they are lengthened for display. Still the short true transfer time is directly indicated with even brighter colors, and notably the normal green color gets brighter and more cyan’ish when very dense traffic is present. In normal MIDI operation the traffic is very sparse, though.