Content

# Protocol Definitions
## MIDI SysEx Message General Format
Per MIDI standard, the SysEx Message layout is :
F0h	: „Start of SysEx“ marker
mmid0 [mmid1 mmid2]	: 1-byte of 3-byte MIDI Manufacturer ID
[data1 [data2 … dataN]]	: 1…N bytes of raw payload (all with Bit7==0!)
F7h	: „End of SysEx“ marker
### MIDI Manufacturer ID:
NLL will use a 3-byte Manufacturer ID that has yet to be requested and granted from midi.org, see https://www.midi.org/request-sysex-id ($240 per year for a simple „non-voting“ membership).
The first byte is zero, indidcating a 3-byte ID. The second byte will most likely be 21h (indicating the second block of ID address space reserved for the „european and others group) and the third byte will be something in the 52h…7Fh range (the free slots in that 2nd block as of Oct. 2020, as per https://www.midi.org/specifications-old/item/manufacturer-id-numbers ).
For the moment, we will use a made-up Manufacturer ID, choosen to be 00h 4Eh 4Ch which happens to be ”\0NL” in ASCII character coding. 4Eh as „group ID“ is most likely unoccupied now and in future and should not cause irritations.
Messages not addressed to a NLL Device (different Manufacturer ID) are simple ignored for device function control.
### Raw Payload:
The raw data payload may consist from zero to any number of bytes, length is determined by the F7h end of sysex marker only. All bytes in the raw payload must have the MSB’s (bit 7) set to zero to keep the MIDI parsers happy (everything > 80h is a „command“ byte).
Nonetheless, the SysEx message may be interleaved with the MIDI real-time messages (command bytes F0h…FFh).
à To reduce parsing effort, a NLL SysEx message shall never contain interleaved real-time messages other than MIDI Clock (F8h). If the parser finds a byte >= 80h (other than F7h and F8h) this is an error condition, possibly causing whatever process to be completely aborted.
à Further, to reduce buffer memory issues in the device, and for a finer transfer interleave granularity on the USB bus, a complete NLL SysEx message should be size-restricted. 1000 or 1024 bytes total size seems to be a practical value. Larger blocks of data must be sent in chunks and a management of those chunks must be implemented.
## NLL Device Control SysEx Message Format
A NLL Device Control SysEx Message, both outgoing and incoming, builds on the standard SysEx with the Manufacturer ID as described above. The raw payload section looks like this:
did	: „Device ID“ number, 7bits(!)
44h 43h	: „Device Control“ ID Bytes (ASCII „DC“);
mid-L mid-H	: „Message ID“ number (low and high byte, 7bits each)
[7-bit encoded message payload]	: optional data payload in the NLL 8-to-7-bit encoding scheme.
### Device ID:
A number ranging from 01h to 7Fh, denoting the NLL Device. Currently, we only have assigned one device: 01h = NLL MIDI Host-to-Host Bridge.
### Message ID Number:
The message ID number is 14 bits, constructed by high byte and a low byte. Both bytes are 7bits and shall range from 01h to 7Fh. The combined value is determined by msg_id = (mid-H << 8) | mid-L, though. That means bits 15 and 7 are always zero.
The message ID’s meaning is device-specific.
### Encoded Message Payload:
If a message contains a payload, it is always encoded in the NLL-specific 8-to-7-bit encoding. By this, any content comprised of 8-bit data can be transferred. The end of the encoded data block is only identified by the F0h end of sysex marker.

## NLL 8-to-7-bit encoding
To transfer arbitrary 8-bit data, the data stream must be encoded in a byte stream where all MSB’s (bit 7) are set to zero to conform to MIDI standard.
Therefore, we use a specific proprietary encoding mechanism. An 8-bit stream is partioned into input blocks of 7 bytes, only the last block may have less than input 7 bytes but should at least have one byte (while an „empty“ 8-to-7-bit encoding is possible – containing only a msbs byte, it is not recommended).
Such an input block of 7 bytes data0…data6 is encoded in the following way into 8 resulting bytes:
msbs lsb0 lsb1 lsb2 lsb3 lsb4 lsb5 lsb6
msbs contains the MSB bits (bit 7) of data0 (at bit position 6), data1 (at bit position 5), …, data6 (at bit position 0). Bit 7 of msbs is always 0, to comply to the 7-bit restriction.
lsbN contains the lower 7 bits of the corresponding dataN input byte.
An incomplete block is allowed as the last block in the message but should contain at least one input data byte, resulting in two encoded output bytes.
In general, the resulting message size of the encoded data of a non-zero input size can be calculated by:
encoded_data_size = (((input_size-1)/7)*8) + (((input_size-1)%7)+2)
For example, a 25-byte input sequence would result in:
msbs1 lsb00 lsb01 lsb02 lsb03 lsb04 lsb05 lsb06 (8 bytes)
msbs2 lsb07 lsb08 lsb09 lsb10 lsb11 lsb12 lsb13 (8 bytes)
msbs3 lsb14 lsb15 lsb16 lsb17 lsb18 lsb19 lsb20 (8 bytes)
msbs4 lsb21 lsb22 lsb23 lsb24 (5 bytes)
        (29 bytes total)
For example, an input stream of
C3 84 5A 7F DC 03 2B E2 4B 92
would result in
69 | 43 04 5A 7F 5C 03 2B | 50 | 62 4B 12
For the first block, 01100100 in binary (69 in hex) denotes the msb's of the data bytes data0, data1, and data4 to be 1.
For the second block we have 01010000 (50), marking msb's of data0 and data2.